## Slide 1
Assessing the hazards and impacts of sea level rise in Virginia
Tal Ezer
CCPO, Old Dominion University, Norfolk, VA, USA
Center for
Coastal Physical Oceanography
Mitigation and Adaptation Workshop
Suffolk, VA, 11-13 August-2015
http://www.odu.edu/ao/research/ccslri/
http://mari.odu.edu/

## Slide 2
Increased coastal erosion
Impacts of rising seas on Virginia’s environment and coasts:
Saltwater intrusion into Virginia’s marshland
Increased damage from storm surges
Increased frequency of tidal flooding
Mitigation and adaptation planning must assess the risks involved in future sea level rise

## Slide 3
Norfolk in 1897 (population ~20,000)
… and Norfolk today (pop. ~250,000)
As the landscape changed, so did the vulnerability and risk associated with sea level rise.
Cruise ship terminal World’s largest Navy base
Chesapeake Bay
Elizabeth River

## Slide 4
We have seen floods in Virginia for many years, but their frequency and severity increased over time…
What factors contribute to local risks?
thermal expansion
melting ice sheets & glaciers
volume change
Glacial Isostatic Adjustment (GIA)
groundwater extraction, hydrology, geology, etc.
Gulf Stream, Atlantic Circulation (AMOC), N. Atlantic Oscillations (NAO)
Norfolk, 1933
Norfolk, 2009
Gulf Stream
In VA/NC: land is sinking while SL is rising
Global Sea Rise
Land Subsidence
Oceanic & Atmospheric Dynamics
MD
VA
NC
Risk: acceleration in Greenland & Antarctic ice melt could be catastrophic…
Risk: local SLR is much faster in VA than farther north or south…
Risk: acceleration of SLR is larger in some locations; unpredictable variations in sea level over short periods…

## Slide 5
Impact of Sea Level Rise (SLR) on local storm surge in Norfolk, VA
Tide gauge data (global)
Satellite
data
Local tide gauge (Norfolk)
Storm surge 
Global SLR
Local SLR
Storm and tide
Post glacial land
subsidence
Recent SLR acceleration due to ocean dynamics

## Slide 6
To prepare for future sea level rise (SLR) we need to know:
What are the trends of SLR in Virginia?
Are they constant or changing?
How are they compared to Global SLR?

## Slide 7
Long (40-110 yrs) sea level records:
increase SLR rate from ~2.4 mm/y (50s-80s) to ~4.5 mm/y (80s-today)
higher SLR in lower CB, ~5.3 mm/y, than upper CB, ~4.3 mm/y and Eastern Shore Peninsula, 3.9 mm/y
1953-1983
1983-2013
Monthly Sea Level
4.08 mm/y
4.31 mm/y
4.14 mm/y
4.88 mm/y
SLR past 30yr
4.39 mm/y
5.86 mm/y
5.55 mm/y
3.93 mm/y

## Slide 8
Short (10-20 yrs) sea level records in VA:
even larger SLR rate, ~5.7 mm/y , in recent years than in long records
6.07 mm/y
5.95 mm/y
5.48 mm/y
5.34 mm/y
4.11 mm/y

## Slide 9
Summary of estimated sea level rise around the Chesapeake Bay:
Rising faster than global SLR and rates increase (acceleration)
SLR (mm/year)
SLR (feet/century)
2 -
3 -
4 -
5 -
6 -
- 1.0
- 2.0
- 1.5
1953-1983
1983-2013
2000-2014
Global SLR past 20yrs
(from satellites)
Global SLR 100 yrs
(from tide gauges)

## Slide 10
Land Subsidence:
due to Post Glacial Rebound the land around VA/NC is sinking
Other contributions to subsidence: sediment compactions, groundwater removal, etc. (Boon et al., 2010)
land uplift
land sinking

## Slide 11
While global sea level is rising, land is sinking (~1.5-3 mm/yr in VA)
Nevada Geodetic Lab
GPS measurement of vertical land movement
Map of land subsidence (USGS)
Post glacial rebound
Underground water extraction (West Point & Franklin paper mills)
Other geological reasons (Chesapeake Impact Crater?)
Paper Mills

## Slide 13: What about Ocean Dynamics? Sea level is not level: ocean currents  sea level slope
The Gulf Stream “pulls” water away from the US coast, keeping sea level on VA coasts ~1-1.5 m (3-5 feet) lower than water offshore.
In warmer climate the Atlantic Ocean circulation is expected to weaken
If the Gulf Stream slows down  coastal sea level would rise!!!
US East Coast
~1m
~100km
European Coasts
Atlantic Ocean circulation

## Slide 14
The Gulf Stream is dynamic and unpredictable
Gulf Stream
(warm, high sea level)
Eddy
Mid-Atlantic Bight
(cold, low sea level)
Norfolk

## Slide 15
Why do stations in different locations show the same pattern?
SL (m)
Decline in Gulf Stream strength since 2004
Acceleration in sea level
Sea Level
Gulf Stream
strength
Chesapeake Bay
Atlantic Coast
Correlation between change in GS and SL:
R=-0.85 (99% conf. lev.)

## Slide 16
Are short-term sea level variations also affected by the Gulf Stream?
Week-long tidal flooding in Norfolk
(no storms!!!)
Weakening Gulf Stream across the Florida Strait is correlated with flooding in Norfolk…
~35% decline in FC transport
FL
 2ft high WL
 Weakening GS

## Slide 17
Consequence of sea level rise: Increase flooding
Chrysler
Museum of Art
flood wall

## Slide 18
flood wall
Despite the risk, new houses are being built in flood-prone streets.
An example of adaptation, but is it a smart planning?....
~6ft

## Slide 19
(SLR=4.5 mm/y)
Today: ~10 full days of flooding per year
2050: ~60 full days of flooding per year
Until the 1970s: ~20 hours of flooding per year

## Slide 20
2012
1933
Chesapeake-Potomac Hurricane of 1933- ~120 mph winds
“Super-storm” Sandy-
~100 mph winds
How would the frequency, path and intensity of tropical storms and hurricanes change in the future?
Even if future storms will not be stronger, SLR would result in higher storm surge and more damage!

## Slide 21
Top storm surges in Norfolk, VA

## Slide 25: Flooding affects universities, navy, commerce, medical facilities, etc.
Old Dominion Univ.
campus
Major road to Naval Station Norfolk
(world’s largest navy base)
to Eastern VA Medical School and Sentara Norfolk General Hospital
Hampton Blvd, Norfolk, VA
 my office

## Slide 26
Major federal facilities in Hampton Roads may be affected by rising seas:
Air bases
Navy bases
Coastguard
NASA Langley
Jefferson Lab
Shipyards

## Slide 27: What can we do to reduce the risk? Adaptation and mitigation options (Note: many European countries are far ahead of the US in developing strategies to address sea level rise- see Amsterdam, Venice, London, etc.)
Source: Nicholls (2010) “Understanding Sea-Level Rise and Variability”

## Slide 28
Example of accommodation: raising houses in Norfolk
Cost: ~$100,000 per house
Repetitive flood damage claims in Norfolk:
(source: Norfolk City Planning Dept.)
2009- ~200 claims
2011- ~750 claims
2012- ~900 claims

## Slide 29
Example of protecting methods:
flood gates in downtown Norfolk (may need more…)
flood gate
flood wall
pumping station

## Slide 30
Future projections of global SLR (e.g., IPCC reports) give too large range for practical local planning….
So we need to do better in projecting local sea level rise and assess the increased risks

## Slide 31: Thank You
before Sandy
after Sandy